RZFD-330T全自动方底手把纸袋机

RZFD-330T Fully Automatic Square Bottom Paper Bag Machine with Handle inline

样品袋

报价单Quotation List

Date ： 2019                                 Validity：30days

| 货物型号及描述 Description | 单 价 Unit Price |
| --- | --- |
| RZFD-330T方底纸袋机 RZFD-330 T Fully Automatic Square Bottom Paper Bag Machine with Handle inline |  |
| 付款条件 PAYMENT TERM | 签订合同即付货款总额的30%预付款，工厂验收合格付清机器全款发货。 After signing of the contract ,the total amount of 30% advance payment, factory acceptance payment before delivery after the machine testing is ok. |
| 发货期 Delivery time | 收到定金后大约90个工作日。工厂在订单确认时会重新决定是否变更交货期。 About 90 working days after receiving the deposit. The factory will decide whether to change the delivery date when the order is confirmed. |
| 电器设备 Electrical equipment | 本机电器设备采用三相380v。如有特殊要求请事先与我公司说明。 This machine adopts three-phase 380v. If you have any special requirements, please explain in advance with my company. |
| 保修 Guarantee | 我们提供为期12个月的保修。在保修期间，我们提供免费更换因质量问题导致的损坏部件。所有因买方使用不当（包括擅自修改PC及触摸屏内置软件）所造成的故障都不在保修范围内。（易损件除外配件易损清单） We offer a 12-month warranty. During the warranty period, we provide free replacement of damaged parts due to quality problems. All failures caused by improper use of the buyer (including unauthorized modification of PC and touch screen built-in software) are not within the scope of the warranty (except for the vulnerable parts of wearing parts). |
| 安装调试 INSTALLATION | 供方安装专业工程师上门安装及设备调试。如买方出国安装及调试，工程师人员费用（含签证，食，住宿，机票及100美元每天工资）由买方支付。Engineers are available to install and debug door to door and overseas. The cost for overseas will be for the buyer’s account, including visa charge, food, accommodation,around air tickets, and salary of 100usds daily one person. |

性能与用途 Properties and uses：

全自动方底纸袋机，用于生产带手挽的手提纸袋。本机特别适用于食品和服装等行业的购物袋批量生产。该机由手挽机将卷绳和纸片卷筒制做成手挽，通过输送系统将手挽送至贴把机组再将原色或印刷好的卷筒纸进行纸绳位预点断、贴片位涂胶、自动粘贴手挽，再由主机将贴有手挽的纸张进行涂边胶、成筒、切断、压痕、底部涂胶、袋底成型并输送出袋，整个过程一次性同步完成。本机采用德国原装进口高速运动控制器（CPU），通过高速总线控制伺服的运行，保证运动稳定，运动曲线平滑，是广大印刷包装厂家首选的全自动手提方底纸袋设备。

Fully automatic square bottom paper bag machine is designed for the production of paper bags with twisted handles. It is suitable for mass production of shopping bags in industries such as food and clothing. The one-line process consists of twisted handles making from paper rolls and twisted rope, delivery of handles to paste unit, pre-cutting of paper on position of rope, patch position gluing, handle pasting, and paper bag making. The paper bag making process consists of side gluing, tube forming, cutting, creasing, bottom gluing, bottom forming and bag delivery. This machine adopts German imported high-speed motion controller (CPU), which controls the operation of servo through high-speed bus to ensure stable movement and smooth motion curve. It is the automatic square bottom paper bag equipment with handles inline preferred by the majority of printing and packaging manufacturers.

主要特点Main features:

1.采用法国SCHNEIDER触摸屏人机界面，操作功能一目了然，便于掌控。

2.采用德国原装LENZE运动控制器（PC），通过与光纤一体化，保证高速运行稳定。

3.采用德国原装LENZE伺服电机搭配德国原装SICK光电眼修正，精确跟踪印刷袋尺寸。

4.原料装卸采用液压自动升降结构，放卷采用全自动恒张力控制。

5.原料纠偏采用意大利SELECTRA，降低纸卷对位调整时间。

1.Use France SCHNEIDER touch screen human-computer interface, making the machine easy to operate and control.

2.Adopt Germany original LENZE PC control, integrated with optical fiber. Thus ensure stable and high speed running.

3.Adopt Germany original LENZE servo motor and German original SICK photoelectric eye correction, tracking printing bag accurately.

4. Raw material loading adopts hydraulic auto-lifting structure. Unwind unit adopts auto tension control.

5.Raw material unwinding EPC adopts Italy SELECTRA, reducing material alignment time.

技术参数  Technical parameter 全：表示全自动

| 机型 Model | RZFD--330T | RZFD--450T | RZFD--450T（B） |
| --- | --- | --- | --- |
| 纸袋裁切长度 Cutting length | 270-530mm | 270-530mm | 380-760mm |
|  | 270-430mm（全） | 270-430mm（全） | 380-660mm（全） |
| 纸袋宽度 Bag width | 120-330mm | 260-450mm | 260-450mm |
|  | 200-330mm（全） | 260-450mm（全） | 260-450mm（全） |
| 袋底宽度 Bottom width | 60-180mm | 80-180mm | 80-200mm |
| 纸袋克重 Paper Thickness | 60-150g/㎡ | 80-150g/㎡ | 80-150g/㎡ |
|  | 80-150g/㎡（全） | 80-150g/㎡（全） | 80-150g/㎡（全） |
| 纸卷宽度 Paper roll width | 380-1050mm | 700-1300mn | 620-1350mm |
|  | 620-1050mm（全） | 710-1300mm（全） | 710-1350mm（全） |
| 纸料直径 Roll paper diameter | ф1300mm | ф1300mm | ф1300mm |
| 纸芯内经 Paper core | ф76mm | ф76mm | ф76mm |
| 手把贴片长度 Patch length | 152mm | 152/190mm | 152/190mm |
| 手把贴片宽度 patch width | 45-50mm | 45-50mm | 45-50mm |
| 手把绳长 Handle length | 320/340mm | 320/340mm | 320/340mm |
| 纸绳间距 Handle distance | 72mm | 72/85mm | 72/85mm |
| 手把纸绳直经 Rope diameter | ф4-5mm | ф4-5mm | ф4-5mm |
| 手把贴片纸卷宽度 Patch paper roll width | 90-100mm | 90-100mm | 90-100mm |
| 手把纸卷直径 patch paper roll diameter | ф1200mm | ф1200mm | ф1200mm |
| 手把贴片纸克重 patch paper thickness | 100-135g/㎡ | 100-135g/㎡ | 100-135g/㎡ |
| 机械速度 Machine Speed | 30-200bags/min | 30-200bags/min | 30-150bags/min |
| 纸袋速度 production speed for bags without handles | 30-180bags/min | 30-150bags/min | 30-120bags/min |
| 带手提速度 production speed for bags with handles | 30-150bags/min | 30-130bags/min | 30-130bags/min |
| 封底方式 Bottom folding type |  |
| 裁切刀具方式 Cutting knife | 锯齿裁切 Sawtooth cutting |
| 总功率 Power Supply | 380V 3Phase 32KW | 380V 3Phase 32KW | 380V 3Phase 37KW |
| 整机重量 Machine weight | 17T | 17.5T | 17.5T |
| 整机尺寸 Machine size | 15000x6000x2700mm | 15000x6000x2700mm |

主要电器元件配置单Main Electrical Components List

| 控 制 系 统 Control System |
| --- |
| 名 称 Name | 数 量 QTY | 产地/ Original | 品牌 Brand |
| CPU编程控制器 CPU Program Controller | 1 | 德国 Germany | LENZE |
| PLC电源模块 PLC Power module | 1 | 德国 Germany | LENZE |
| PLC输入模块 PLC Input module | 2 | 德国 Germany | LENZE |
| PLC点卡 PLC Point card | 1 | 德国 Germany | LENZE |
| 主电源滤波器 Main power filter | 1 | 德国 Germany | LENZE |
| 人机界面触摸屏 Human-computer touch screen interface | 1 | 法国 France | SCHNEIDER |
| 伺服电机 Servo Motor | 7 | 德国 Germany | LENZE |
| 伺服电机减速机 Servo Motor Reducer | 7 | 德国 Germany | 阿尔法 |
| 伺服驱动器 Servo driver | 5 | 德国 Germany | LENZE |
| 纸袋定型变频器 Bag forming frequency converter | 1 | 瑞士 Switzerland | ABB |
| 纸袋定型电机 Bag forming motor | 1 | 台湾 Taiwan |  |
| 印刷跟踪光电眼 Photoelectric eye for printed-bag tracking | 1 | 德国 Germany | SICK |
| 光纤通信分离器 Optical fiber communication separator | 1 | 美国 USA |  |
| 低压电器 Low voltage electrical apparatus | 1 | 法国 France | SCHNEIDER |
| 光电传感器 Photoelectric sensor | 1 | 美国 USA | BAUMER |
| 气动元件 Pneumatic component | 1 | 中国台湾 Taiwan |  |
| 自动贴加润滑油 Auto lubricating | 1 | 中国 China |  |
| 配电柜带自动恒温空调柜 Air conditioner for electric control box | 1 | 中国 China |  |
| 放卷 纠偏、张力控制系统 Deviation correction and tension control system |
| 名 称 Name | 数 量 QTY | 产地 Original | 品牌 Brand |
| 纠偏控制器 EPC controller | 1 | 意大利 Italy | SELECTRA |
| 伺服纠偏电机 Servo motor for EPC | 1 | 意大利 Italy | SELECTRA |
| 超声波感应器 Ultrasonic sensor | 1 | 意大利 Italy | SELECTRA |
| 磁粉制动器 Magnetic powder brake | 1 | 中国 China | WEIZHENG |
| 磁粉自动张力系统 Automatic Tension System of Magnetic Powder | 1 | 德国 Germany | LENZE |
| 自动液压上料电机 Automatic Hydraulic Feeding Motor | 1 | 中国台湾 Taiwan |  |
| 上料液压油缸 Feeding hydraulic cylinder | 1 | 中国 China |  |
| 传动 Transmission |
| 名 称 Name | 数量 Qty | 产地 Original | 品牌 MTED |
| 同步带 Synchronous belt | 1 | 中国 China | BELDI |
| 同步轮 Synchronous wheel | 1 | 中国 China | MTED |
| 轴承 Bearing | 1 | 德国 Germany | FALA |
| 导辊 Guide roller | 1 | 中国 China | BAIXIAO |
| 齿轮 Gear | 1 | 中国 China | MTED |
| 胶水部位 Glue position |
| 名 称 Name | 数量 Qty | 产地 Original | 品牌 MTED |
| 底部胶（糊底白乳胶） Bottom glue (bottom-sealing white latex) | 1 | 中国 China | MTED |
| 底部匀胶电机 Motor for bottom glue evening | 2 | 中国 China |  |
| 自动气动灌胶阀 Pneumatic auto glue filling valve | 2 | 中国 China |  |
| 底胶胶位检测 Glue Glue Position Detection | 1 | 瑞士 Switzerland | BAUMER |
| 中锋水性喷胶枪 Spraying gun for center sealing (dense adjust Glue gun ) | 1 | 中国 China | MTED |
| 水性白乳胶高压喷胶桶 High-pressure glue barrel for white latex | 2 | 中国 China | MTED |
| 贴手把部位 Handle Pasting Unit |
| 名 称 Name | 数量 Qty | 产地 Original | 品牌 MTED |
| 纠偏控制器 EPC controller | 2 | 意大利 Italy | SELECTRA |
| 伺服纠偏电机 Servo motor for EPC | 2 | 意大利 Italy | SELECTRA |
| 超声波感应器 Ultrasonic sensor | 2 | 意大利 Italy | SELECTRA |
| 热熔胶机 Hot Melt Glue Device | 1 | 瑞士 Switzerland | RO |
| 热熔胶枪 Hot Melt Glue Gun | 2 | 瑞士 Switzerland | RO |
| 热熔胶管 Hot Melt Glue Gun | 2 | 瑞士 Switzerland | RO |
| 手挽伺服电机 Hand-held servo motor | 1 | 德国 Germany | lenze |
| 手挽伺服驱动机 Hand-held Servo Driver | 1 | 德国 Germany | lenze |

注: 本合同中之机器所使用的采购件在设备升级或更新时，用不低于现有品牌质量的同级品牌替代，卖方将保留权利，不再另外通知。

Note:The purchased parts used in this machine will be replaced by the same-level brand that is not lower than the existing brand quality when the equipment is upgraded or updated. The seller will reserve the right without further notice.